## Slide 1: Hydrologic modeling applications in wildfire management
Zack Holden – Research Ecologist, RMRS Fire lab, Missoula, MT
Allen Warren – U. Montana
Alan Swanson– U. Montana
Kimberley Davis – RMRS Fire Lab
Solomon Dobrowski – U. Montana
Marco Maneta – U. Montana
Matt Jolly RMRS firelab
Charlie Luce RMRS, Boise
Kelsey Jencso, U. Montana
Zachary Hoylman, U. Montana
Ellen Jungck, USFS Region 1
Vince Archer, USFS Region 1
Lolo Peak fire, July-August 2017

## Slide 2
fuels/vegetation
terrain
weather/climate
Fire management space
1980’s climate

## Slide 3: Nez Perce Clearwater Priority Landscape historical precipitation
DRY WET
Warm season (may-sept) standardized precipitation index (SPI)

## Slide 4
Fuels/vegetation
terrain
Drought, climate change and extreme weather shrink weather windows for managing fire
weather/climate
Drought
Climate change
Weather extremes
Current/future climate
Challenging conditions
-Longer fire seasons
-Higher atmospheric aridity/temperature
-Less summer precipitation
-Longer periods without rain
-Drier fuels
-Fewer days meeting burn prescriptions

## Slide 5
Fuels/vegetation
terrain
Drought, climate change and extreme weather shrink weather windows for managing fire
weather/climate
Drought
Climate change
Weather extremes
Current/future climate
Challenging conditions
-Longer fire seasons
-Higher atmospheric aridity/temperature
-Less summer precipitation
-Longer periods without rain
-Drier fuels
-Fewer days meeting burn prescriptions

## Slide 6
Fuels/vegetation
terrain
Climate feedbacks to vegetation increase fuel complexity and hazard
More dynamic, complex fuels
More dead biomass
Drought
Climate change
Weather extremes
weather/climate
Western forests adapted to wet periods of the 1980’s-90’s are still responding to the last decade of drought.
-trees vulnerable to insects/disease
-Increased tree mortality
-more dead surface fuel

## Slide 7
Fuels/vegetation
terrain
precision agriculture principals to deal with shrinking operating space?
high resolution
forecasts
weather/climate
microclimate
Precision fuel moisture
and temperature model
Precision silviculture
LiDAR, 3D fuel maps

## Slide 8
Fuels/vegetation
terrain
precision agriculture principals to deal with shrinking operating space
Hydrology
Vegetation stress, live
Fuel moisture content
high resolution
forecasts
weather/climate
microclimate
Precision fuel moisture
and temperature model
Precision silviculture
LiDAR, 3D fuel maps

## Slide 9
Review Findings
Insufficient consideration of the impact of long-term drought on prescribed fire behavior.
Not using available forecasting tools or insufficient training in using them.

## Slide 10
stopped running in 2020
NASA A.35 Applied Science / Wildfire Applications (2014-2018)
Co-PI’s Matt Jolly, Russ Parsons, Marco Maneta, Erin Landguth
Allen Warren
Alan Swanson
U. Montana

## Slide 11
Historical soil water balance data
Daily 250 meter grids 1981-2020
30 year climatology/downscaled to 30m for Region 1
Vegetation mapping, modeling
Lolo, Montan 2017

## Slide 12
Hoylman et al. (in revision) Optimizing drought assessment for soil for moisture deficits (Water Res. Res.)
NOAA/NIDIS funding-2018-2021; drought indicators of soil moisture
Zack Hoylman
U. Montana

## Slide 13
NOAA/NIDIS support 2021-2024
High resolution soil moisture modeling for drought an wildfire management
Marina Skumanich, Britt Parker

## Slide 14
NOAA/NIDIS support 2021-2024 -Operational daily snow and soil moisture model
- Daily 250 meter soil moisture anomaly + 3 day forecast
- modified Keetch-Byram Drought Index in development (co-I Matt Jolly)
- planned link to drought.gov
Notes: Use cartoon table to show how I measure things.

## Slide 15: Ecohydrology models
Simulate surface energy/moisture exchange
-Ground surface temperature
-Soil moisture (3 layers)
-Ground temperature
- Evapotranspiration
~ Runoff (ech2o)
Maneta and Silverman 2013
Frankenstein and Koenig 2004

## Slide 16
National Science Foundation Geography Grant: Solomon Dobrowski, P.I. (2017-2019)
Marco Maneta
Anna Sala
Solomon Dobrowski

## Slide 17: Simulating plant hydraulics with ech2o
Gerard Sapes, Anna Sala, University of Montana
Ponderosa pine seedling dry down Experiments

## Slide 18
Daily weather grids
Hourly point timeseries
ECH20 model Obs. soils
SOIL MOISTURE CALIBRATION
SOIL TEMPERATURE VALIDATION
adj soils ECH20 model MODIS LST
≈
Raw gridded soils
30m dem routing
MODEL INPUTS
Ech2o model calibration and validation
-Calibrated to soil moisture
-Validation with MODIS surface temperature
NASA Sustainability Grant: Solomon Dobrowski, P.I. (2018-2021)
650 soil moisture stations

## Slide 19: Ech2o skin temperature validation with MODIS
2,200 sites with < 5% canopy cover
2002-2018 (1.2 million obs)
Ech2o simulated soil surface temperature vs. MODIS LST
Zack Hoylman
U. Montana

## Slide 20: 2017 Lolo Peak Fire, MT low elevation, south facing
DNBR
Simulated soil moisture and plant hydraulic stress

## Slide 21
Vegetation effects on snow, soil moisture and surface temperature and interactions with terrain (i.e. topoclimate, microclimate)

## Slide 22: Evaluating soil moisture as an indicator of fire danger and spread potential in the U.S. Northern Rocky Mountains
Review Findings
Insufficient consideration of the impact of long-term drought on prescribed fire behavior.
-Simple water balance, uniform veg,
No lateral flow
-Energy balance model, dynamic veg,
routing, bedrock leakance, etc.

## Slide 23
Annual forested area burned (1984-2020)

## Slide 24: Annual forested area burned (1984-2020)

## Slide 25: With hindsight, area burned is well predicted by weather data, models

## Slide 26
VIIRS satellite thermal fire detections; 375m 2x daily, 2012-present
spatial regression to estimate daily day of burn at 250m resolution
207 fires from 2012-2021
2017 Lolo Peak fire
2016 fire

## Slide 27: Daily weather, fuel and hydrologic predictors
Water supply
Topofire soil moisture (raw, anomaly)
Ech2o Soil moisture, soil surface temperature, leaf water potential
ERC, 100 and 1000 hour fuel moisture
Atmospheric demand
Potential ET (PET), deficit (DEF), tmax, rhmin, VPDmax, solar radiation
Nocturnal humidity
Tmin, Rhmax, VPDmin, Dewpoint temperature
Wind speed variables
Hourly Real time mesocscale analysis (RTMA) 2.5 km resolution(mean, max, 95th ptile)
Climate Forecast System Reanalysis (CFSR) 35 km resolution
Nearest RAWS station wind
Vegetation/Fuels: Forest, Grass, Shrub fractions from RAP
- 25 variables extracted for daily burn footprint
- predictors grouped to limit autocorrelation
207 Fires

## Slide 28: 5 year ech2o simulations for each fire Rangeland Analysis Platform (RAP) canopy cover (Allred et al. 2021)

## Slide 29: Per-fire correlations between daily spread and weather, hydroclimate

## Slide 30
variable names | Nvar | R-squared | MAE
Full model - all variables |  |  | 
TSKIN + LWP + TSKIN + forest-cover + ERC + TDEW + AtmPress | 6 | 0.464 | 0.678
TSKIN + LWP + forest-cover + ERC + TDEW | 5 | 0.461 | 0.683
TSKIN + forest_cover + ERC + TDEW | 4 | 0.454 | 0.688
operational model - Ech2o and fuel moisture variables excluded |  |  | 
SOIL_anom + DEFICIT +VPD_night + forest-cover + AtmosPress | 5 | 0.345 | 0.777
SOIL_anom + forest-cover+ Rhmin + TMIN | 4 | 0.344 | 0.793
Boosted regression tree model results
- 260,000 candidate models, only variable per group
- full models vs. easily operational

## Slide 31: Key results from fire spread modeling
Simulated surface temperature and LWP strongest predictors
Energy balance models contribute significant information
Hydraulic stress slightly better predictor than soil moisture
Wind effects negligible
nighttime humidity consistent strong predictor
(Balch et al. 2022; Freeborn, Jolly et al. 2022)

## Slide 32: Operational mapping for Region 1 https://topofire.dbs.umt.edu/public_data/R1_fire
Erin Noonan, R1 fire analyst
1-3 day forecast maps
-fire growth probability
- predicted acres growth
- soil moisture
- wind speed
- surface weather

## Slide 33: Hurricane Dora
Major precipitation event August 1st-6th
.25-5 inches of rain across the N. Rockies

## Slide 34: Soil moisture anomaly response to precipitation

## Slide 35: Active VIIRS fires August 1st-6th 2023 Daily potential area burned predictions

## Slide 36: Where are we going?

## Slide 37: Web-based fire spread forecasting tool
https://topofire.dbs.umt.edu/firespread_jobs/firespread_modeling
Adam Viray
Erin Landguth

## Slide 38
On demand fire spread predictions
1-3 day hourly wind, weather, soil moisture forecasts
Bipartisan Infrastructure proposal to develop system for Rx burn and planning
Add ensemble physics based models
-QES-fire (M. Moody), QUIC-fire, others?
Ensemble model forecasts?

## Slide 39: post-fire reforestation in the western United States
Zack Holden – USFS Region 1
Allen Warren – U. Montana
Ellen Jungck – USFS Region 1
Alan Swanson– U. Montana
Marco Maneta – U.Montana
Kim Davis – U.Montana
Vince Archer – USFS Region 1
Shelagh Fox – USFS Region 1
Nicole Ballofet- USFS, Washington DC
Lolo Peak fire, July-August 2017

## Slide 40
Ballofet and Dumroese 2022
Forest Activities database (FACTS)
Massive increase in unmet reforestation needs due to wildfires
post-fire reforestation in the western United States

## Slide 41
REPLANT act mandates addressing reforestation backlog over next decade
Removes cap on reforestation trust fund and increases annual funding from $30mil to $140 mil or more.
Once in a generation opportunity to shape future forests

## Slide 42: Surface temperature as biophysical constraint on low elevation tree line
brief exposure to temperatures of 55 °C can kill conifer seedlings
Cambial damage and girdling;
lose ability to move water from soil to atmosphere

## Slide 43: 30 meter surface temperature mapping
75,000 random stratified points
Spatial domain around each point to allow lateral water flow
Ech2o run hourly from 1982-2018
Calculate climatological average annual maximum skin temperature at each point
Geographically weighted regression used to fit/predict across western U.S.
Computational resources and support from the University of Montana’s Griz Shared Computing Cluster (GSCC)

## Slide 44: Potential soil surface temperature (PSST) -95th percentile maximum annual soil surface temperature for a bed of 2 inch ponderosa pine seedlings 30 meter resolution raster - historical (1982-2018) - future (2050) from CMIP6 ensembles
Holden et al. (in review)

## Slide 46: https://orthanc.dbs.umt.edu/regenmapper

## Slide 49: Simple automated GIS
Fitted regression models from 2 datasets
- any species prediction
- individual species models for:
PIPO, PSME, PICO, PIEN, ABLA, ABGR
10,000+ plots from 330 wildfires
89 plots, 32 fires; annual recruitment date
Kim Davis Lewis Faller
Kim Davis , RMRS Fire lab

## Slide 50
Full model includes distance to seed from GEDI LiDAR
Climate-only effect model
Dispersal only effect model
Binary outcome (yes, no)
Projected 2050 regeneration probability based on CMIP6 ensemble
post-fire recruitment model for any species

## Slide 51
Administrative priorities for USFS
Planting logic applied to raster
Highest priority with pre-existing FACTS need
Different classification for wilderness, roadless or specially designated area
Planting versus natural regeneration determined using modeled regeneration probability

## Slide 52
calculated for every severely burned pixel
30 meter raster output
Distance to nearest road

## Slide 53
Planting prioritization/optimization

## Slide 54: Where are we going?

## Slide 55
- USDA Agriculture and Forest Research Initiative (AFRI)
- 3 year grant; 2022-2024 $695,000
“Quantitative prediction and prioritization for reforestation success: Development of an automated decision support tool for the USDA Forest Service”
Further develop cost-benefit prioritization
Potential links to ForSys model (Mark Finney, Michelle Day)
Marco Maneta
Allen Warren
Solomon Dobrowski Erin Landguth
Alan Swanson
Kim Davis Lewis Faller

## Slide 56: Web-based ech2o model
On demand point or watershed simulations
Ask questions about post-harvest water and energy
USFS Region 1 funding (Vince Archer, Andy Efta)

## Slide 57: Web-based ech2o model
On demand point or watershed simulations
Ask questions about post-harvest water and energy

## Slide 58
North Superior project (Carli Anaballi)
public comments on post-harvest regen

## Slide 59: Thank you
Funding
NASA
NOAA/NIDIS
USFS Region 1
Computing
U. Montana Griz Cluster
NASA HPC
NSF-Stampede
Many collaborators